## Slide 1: Bits and Bytes

## Slide 2: BIT
Modern computers are binary:
  Everything is represented as being in one of two possible states:
    the state of being a 1
    the state of being a 0
  A bit is the name for this smallest unit of storage in a computer.
    Bit is sort-of derived from "Binary digIT".
Notes: So there are only two possible values for a bit, 0 or 1.
1 = On = Electricity flows
0 = Off = Electricity off

## Slide 3: Digital
Marketing and advertising folks have decided to characterize anything that is based on bits as being "digital".
  Digital Cable TV
  Digital Telephone
  Digital Camera
  Digital Audio
A better name might be “discrete” - digital information is broken up into discrete pieces; it is not continuous. (Your fingers (digits) are used for discrete counting)

## Slide 4: Byte
An ordered sequence of 8 bits (an octet)
Modern computers are based on memory systems organized as bytes of memory
Memory sizes are typically given in numbers of bytes:
  e.g. 16G vs. 32G iPhone
kilobyte | 210 bytes | 1024 bytes | ≒ a thousand bytes
megabyte | 210 kilobytes | 220 bytes | ≒ a million bytes
gigabyte | 210 megabytes | 230 bytes | ≒ a billion bytes
terabyte | 210 gigabytes | 240 bytes | ≒ a trillion bytes
petabyte | 210 terabytes | 250 bytes | ≒ a million billion bytes
exabyte | 210 petabytes | 260 bytes | ≒ a million trillion bytes

## Slide 5: Why an 8-Bit Byte?
Some hardware systems used 4, 5, 6, 7, 9 and even 16 bit bytes. (Some today use a 40 bit byte.)
Why did we settle on an octet?
  Powers of 2 are convenient when working in a binary system: 2, 4, 8, 16
  We need a large enough byte to handle character sets
    24 = 16 values... not big enough
    28 = 256 values... big enough
  0/1 or On/Off or yes/no is helpful
    Electricity can be on or off
Notes: Hanzi?, Kanji? Need more than 256

## Slide 6: 64 bit machine
A machine that processes information in 64 bit chunks.
The processor simply transports the information 64 bits at a time
The data-path, or bus, that runs to and from the processor is 64 bits wide.
8 bits still = 1 byte a 64 bit machine transports 8 bytes at a time
Notes: Fascinating to note that the first 64 bit machine was introduced in 1961, the IBM 7030 Stretch supercomputer. Were made mainstream in 2003 with the x86-64 and 64-bit PowerPC processors.

## Slide 7: How many possible values can one byte hold?
A byte is a sequence of 8 bits, and each bit can hold only two values (0 or 1).
How many sequences (permutations) of ones and zeros are possible?
Here are a few: 00000000 00010000 10000000 10101010

## Slide 8: # of byte values: derivation
2 x 2 x 2 x 2 x 2 x 2 x 2 x 2
# of permutations = 28 = 256
There are 256 possible byte values.
Q: what is the largest actual value held in a byte?
1 | 0 | 0 | 1 | 1 | 1 | 0 | 1

## Slide 9: Understanding Bases
We are familiar with base ten and its “places”
In base ten, the value 10,423.9 can be imagined as
This is a way to visualize the numbers in their places (it is not division). The value could be more accurately expressed as
(1*104) + (0*103) + (4*102) + (2*101) + (3*100) + (9*10-1)
1 |  | 0 | , | 4 |  | 2 |  | 3 | . | 9
104 (10,000) |  | 103 (1,000) |  | 102 (100) |  | 101 (10) |  | 100 (1) |  | 10-1 (1/10)

## Slide 10: Binary Numbers
We can talk about byte values by treating a byte as a base 2 number and converting to base 10 (decimal):
64 + 16 + 4 + 2 = 86 (0*27) + (1*26) + (1*25) + (0*24) + (0*23) + (1*32) + (1*21) + (0*20)
010101102 = 8610
0 |  | 1 |  | 0 |  | 1 |  | 0 |  | 1 |  | 1 |  | 0
27 (128) |  | 26 (64) |  | 25 (32) |  | 24 (16) |  | 23 (8) |  | 22 (4) |  | 21 (2) |  | 20 (1)

## Slide 11: Binary Numbers
Converting decimal to any base can be done by dividing by the base and setting aside the remainder.
So to convert base 10 to base 2:
Divide | Remainder
2 86 | 0
43 | 1
21 | 1
10 | 0
5 | 1
2 | 0
1  carry it over | 1
Then, gather up the remainders from the bottom up:
8610 = 10101102
∟
∟
∟
∟
∟
∟

## Slide 12: Hexadecimal
Base 16 is also convenient for representing byte values. Each group of 4 bits corresponds to a single hex digit.
Decimal | Binary | Hex | Decimal | Binary | Hex
0 | 0000 | 0 | 8 | 1000 | 8
1 | 0001 | 1 | 9 | 1001 | 9
2 | 0010 | 2 | 10 | 1010 | A
3 | 0011 | 3 | 11 | 1011 | B
4 | 0100 | 4 | 12 | 1100 | C
5 | 0101 | 5 | 13 | 1101 | D
6 | 0110 | 6 | 14 | 1110 | E
7 | 0111 | 7 | 15 | 1111 | F

## Slide 13: Hex Example: RGB Values
Red, Green, Blue values used in additive color are commonly represented by hex values, one byte of information per color (e.g. in CSS):
000000 (black) to FFFFFF (white)
166 = 16 million colors (16.8 million, really) For example, solid red is: Red Green Blue FF 00 00
Q: How many values of Red are possible?

## Slide 14: Decimal-Binary Fill-In
Base 10 | Binary
247 | 
 | 10001001
 | 00010000
255 | 

## Slide 15: Decimal-Binary Fill-In
Base 10 | Binary
247 | 11110111
137 | 10001001
16 | 00010000
255 | 11111111